## Slide 1: Quantum simulation with trapped ions at NIST
Dietrich Leibfried
NIST Ion Storage Group

## Slide 2: NIST Penning trap (J. Bollinger, B. Saywer, J. Britton)
side view
CCD camera
ca. 4500 trapped and laser cooled ions:
electronic wave-function 0.1 nm
motional wave-function 80 nm
ABAB plane stacking
in-plane spacing ca. 20 mm
vacuum enclosure
axial cooling beam
B
radial
cooling beam
top view
CCD camera
side view
top view
Porras&Cirac, PRL 96, 250501 (2006)
see Mike Biercuk’s talk

## Slide 3
m1
m2
n
Coulomb interaction:
for oscillating charges constitute two dipoles
quantum mechanically:
spin-spin interactions from Coulomb-coupling
sidebands couple internal states to dipole:
r1
r2
BSB RSB

## Slide 4: arbitrary 2D “spin”-lattice: bottom-up
2D lattice of ions, cooled and optically pumped by lasers
optimized surface electrode trap array
lasers/microwaves implement interactions (Sørensen Mølmer type+phase gates)
sidebands
gate interactions

## Slide 5: surface electrode trap basics
radial confinement:
asymmetric 5 wire trap
axial confinement:
J. Chiaverini et al.,
Quant. Inform. Comp. 5, 419439 (2005)
electric field
electric potential
pseudo-potential

## Slide 6: toy model array
3 infinitely long “5-wire” traps
wire pairs move together

traps pushed up, depth vanishes

naïve approach will only work if
ion height << site distance
(dashed line: single 5 wire trap)
add then square!
ion to surface distance
potential depth/ideal quadrupole

## Slide 7: optimized array electrodes (Schmied, Wesenberg, Leibfried, Phys. Rev. Lett. 102, 233002 (2009)
normalized to depth of ideal 3D-Paul trap and curvature of an optimal ring trap
J. H. Wesenberg, Phys. Rev. A 78, 063410 (2008)

## Slide 8: example model: hexagonal Kitaev
1 ion per site
dipole-dipole interaction
finite along blue
vanish along green/red
2 sub-lattices (cyan/orange)
electrode boundary conditions
sxsx (blue)
sysy (green)
szsz (red)
A. Kitaev, Anyons in an exactly solvable model and beyond, Annals of Physics 321, 2 (2006)

## Slide 9: Kitaev implementation
1 ion per site
dipole-dipole interaction
along blue ≈ 1
along green/red ≈ 0.0025
2 sub-lattices (cyan/orange)
electrode shapes optimized
sxsx (blue)
sysy (green)
szsz (red)
Schmied, Wesenberg, Leibfried, New J. Phys. 13, 115011 (2011)
gnd
rf

## Slide 10: towards implementation
experiments- the places theories go to die.
unknown physicist

## Slide 11: 4K cryogenic ion trap apparatus (built by K. Brown, C. Ospelkaus, M. Biercuk, A. Wilson)
CCD and PMT
(outside vacuum)
bakeable “pillbox” (internal vacuum system)
imaging optics
ion trap
LHe reservoir
radiation shield
optical table with central hole

## Slide 12: inside the copper pillbox
rf/microwave feedthroughs
oven shield
filter board with low-passes
90% transparent gold mesh
view from imaging direction, Schwarzschild objective removed
Notes: 12

## Slide 13: multi-zone surface electrode trap (K. Brown, Yves Colombe)
trap axis
center section of trap chip
≈ 10 mm gold on crystalline quartz
4.5 mm gap-width
Notes: 13

## Slide 14: axial potentials
good approximation for all experiments:
a
distance from symmetry center/mm
potential/eV
a>0, b=0
a=0, b>0
a<0, b>0
Notes: 14

## Slide 15: generalized normal modes
good approximation for all experiments:
generalized equilibrium condition:
(ion distance d)
generalized normal modes:
(small oscillations << d)
a and b determine equilibrium distance and normal mode splitting
normal mode splitting given by (dipole-dipole) Coulomb-energy at distance d
fundamental character of oscillations independent of a and b
entangling gates can be implemented in the same way for all a and b
special cases:
Notes: 15

## Slide 16: perturbed separate wells, avoided crossing of normal modes
exchange frequency
example: homogenous electric field displaces ions in symmetric potential

## Slide 17: reality check: Coulomb vs. heating
ion-ion or ion-surface distance/mm
interaction or heating rate/kHz
Wdd (Be+, 5 MHz ,40 mm dist.)
heating rate old trap chip
heating rate new trap chip
heating rate 300 K sputter-trap
Johnson noise slope (1/d2)
array design rule:
ion-ion distance ≈ ion-surface distance
K. R. Brown et al.,
Nature 471, 196 (2011).
Johnson noise varies widely with
filtering, electrode resistance
etc., line just to guide the eye

## Slide 18: mapping the avoided crossing
experiment:
cool both ions to ground state
probe red sideband (RSB) spectrum for different well detuning
tune wells through resonance by changing potential curvatures (sub-mV tweaks)
8 kHz

## Slide 19: coupling on resonance
18+ quantum exchanges
Tex = 80 ms
30 mm well separation
see also:
M. Harlander et al., Nature 471, 200 (2011)
K. R. Brown et al., Nature, 471, 196 (2011)
experiment:
cool both ions to ground state
insert one quantum of motion with BSB on right ion
attempt to extract quantum of motion after time on resonance

## Slide 20: single sideband gate
strong Carrier
(laser or microwave)
single Sideband
single sideband gate
Bermudez et al., Phys. Rev. A 85, 040302 (2012)
analogous proposals for cavity QED
E. Solano et al., PRL 90, 027903 (2003)
S. B. Zheng, PRA 66, 060302R (2002)
carrier and motional frequency fluctuations suppressed
carrier phase not relevant (if constant over gate duration)
full microwave implementation possible
a > 0, b=0: “conventional” two-ion gate
in single well:
a<0, b>0: “double well” two-ion gate:
arbitrary confining a, b analogously
d
d
detuning between modes
adds phase space areas
d
detuning close to one mode

## Slide 21: gate over coupled wells (A. Wilson, Y. Colombe et al.)
two 9Be+ ions in separate wells
cryogenic surface trap at 4 K
nCOM=4.13 MHz; mode splitting 8 kHz
COM heating: dn/dt= 200 quanta/s
Str heating: dn/dt = 200 quanta/s
30 mm
single sideband gate on both modes
entangled state fidelity: 81%
populations: 91%
parity visibility: 73%
leading sources of imperfection:
double well stability: ≈ 6%
beam pointing/power fluct. ≈3%
state preparation/detection: ≈3%
spontaneous emission: ≈2%

## Slide 22: NIST ion storage group (March 2013)
Manny Knill (NIST, computer science)
Dietrich Leibfried
David Leibrandt
Yiheng Lin (grad student, CU)
Katy McCormick (grad student, CU)
Christian Ospelkaus (postdoc, now Hannover)
Till Rosenband
Brian Sawyer (postdoc, JILA)
Daniel Slichter (postdoc, Berkeley)
Ting Rei Tan (grad student, CU)
Ulrich Warring (post-doc, U Heidelberg)
Andrew Wilson (post-postdoc, U Otago)
David Wineland
David Allcock (postdoc, Oxford)
Jim Bergquist
John Bollinger
Ryan Bowler (grad student, CU)
Sam Brewer (postdoc, NIST)
Joe Britton (postdoc, CU)
Kenton Brown (postdoc, now GTech)
Jwo-Sy Chen (grad student CU)
Yves Colombe (postdoc, ENS Paris)
Shon Cook (postdoc, CSU)
John Gaebler (postdoc, JILA)
Robert Jördens (postdoc, ETH Zuerich)
John Jost (postdoc, now ETH Lausanne)